Pre-processing using MNE (only for 64 channel experiments)

Interpolate bad electrodes

Laplacian re-reference

Load data (specific to each experiment)

Load data from one channel – save as numpy array

Get triggers from .vmrk file – save as numpy array

Sort triggers into different conditions/frequencies

Common analysis functions

Filters: e.g. low pass filter to remove slow drifts

A function to determine if a segment of data is good and can be used in the SSVEPs by checking for e.g. eye blinks. To be called by following functions.

Segment data using triggers and average to make an SSVEP.

Segment data using triggers as above, randomly shuffle the data in each segment, and then average to make an SSVEP. This is one way of calculating signal-to-noise ratio.

Linear interpolation of trigger artefacts (will probably need a function to plot SSVEPs before and after, to check it worked).

Make induced FFT: Segment data into segments of a given length, do an FFT on each segment and then average the FFTs.

Make evoked FFT: Segment data into non-overlapping segments of a given length, each time locked to a trigger. Then average and do an FFT on the average.
Analysis functions

Permutation tests on two conditions: make two SSVEPs by randomly assigning segments from condition 1 and condition 2 to two make two groups, and compare the difference in amplitude. Repeat this may times (e.g. 1000) and create a distribution of amplitude differences, which can be compared to the true difference.

Permutation tests on signal-to-noise: Make SSVEPs using a random subset of triggers (start with a small number), repeat many times (e.g.1000). Then repeat entire test with a different number of segments. Progressively increase number of segments and keep track of the resulting SSVEP.

Simulated SSVEPs (for data without flicker): add a simulated SSVEP (e.g. a sine wave) to the data and create a numpy array of “trigger times”, such that the data can be used with the above functions.

Plots: common function for plotting example SSVEPs in to publication ready figures